## System Components and Wiring Configuration
## IoT Tomato Soil Monitor System – Components, Roles, and Wiring
Component	Role in the System	Connections (Arduino / Power)	Explanation of Integration
Arduino Uno	Central controller (“brain”)	USB / 5V input, GND, A0, A1, D7, SDA, SCL	The Arduino Uno reads sensor data, applies threshold logic, updates the LCD display, and controls the relay that activates the water pump. It coordinates all system behaviour.
Capacitive Soil Moisture Sensor	Detects soil moisture level	VCC → 5V, GND → GND, Signal → A0	Measures the moisture content of the soil. Readings are used to classify soil as dry, optimal, or overwatered. When dry conditions are detected, the Arduino triggers watering.
Water Level Sensor	Monitors water reservoir level	VCC → 5V, GND → GND, Signal → A1	Ensures that water is available before pumping. If the reservoir is empty, the system displays a warning message.
LCD1602 RGB Display (I2C)	User feedback and data visualisation	VCC → 5V, GND → GND, SDA → A4, SCL → A5	Displays real-time system status, including soil condition (dry/OK/overwatered) and water tank state. Provides clear, user-friendly feedback without needing a computer.
Relay Module	Electrical isolation and switching	VCC → 5V, GND → GND, Control → D7	Acts as a safe electronic switch. The Arduino controls the relay to turn the pump on or off without exposing low-voltage logic to high-current loads.
Water Pump	Irrigates the plant	Battery + → Pump +, Pump − → Relay COM/NO	Physically transfers water from the reservoir to the soil when activated. Controlled indirectly by the Arduino through the relay module.
Battery Pack	Power source for pump	Battery + → Pump / Relay, Battery − → Relay	Provides sufficient current to operate the pump independently from the Arduino, preventing voltage drops or damage to the logic circuit.
Breadboard	Prototyping and integration platform	Shared power rails	Allows modular, non-permanent connections between components. Enables rapid testing, debugging, and adjustment during development.
Repurposed Tool Caddy (Enclosure)	Physical housing	N/A (mechanical enclosure)	Protects electronics from splashes, separates water and logic components, and improves portability and safety. Supports the project’s practical and upcycled design narrative.

## System Wiring Strategy Explanation

The system is deliberately divided into two electrical domains:
Logic Circuit (Low Power – 5V)
- Powered by the Arduino
- Includes:
  - Soil moisture sensor
  - Water level sensor
  - LCD display
  - Relay control pin
- Ensures stable sensor readings and display output

Power Circuit (High Power – Battery)
- Powered by a separate battery pack
- Includes:
  - Relay contacts
  - Water pump
- Prevents electrical noise and voltage drops during pump activation

The relay acts as the bridge between these two circuits, allowing the Arduino to safely control the pump without direct electrical connection.

## Battery Life Estimation (Pump Circuit)
Assumptions:
- Battery pack: 4×AA batteries ≈ 2000 mAh
- Average pump current contribution: ~75 mA
Estimated battery life:

Because the pump is not active continuously, in realistic demonstration or intermittent use:
Several days to over one week of operation is achievable.